## Slide 1: WiSync: An Architecture for Fast Synchronization through On-Chip Wireless Communication
Sergi Abadal etc. UIUC
Demo by Han Shen

## Slide 2: Motivation
Recent advances in CMOS RF technology
Challenges in shared-memory programming
  Frequent read-n-write of global variables
  Mutual exclusion lock
  Repeated broadcast/reductions(Data Communications)
Previous work
  Hardware support: Barrier Network(Cray T3D), Synchronization register(Cray T3E)
  Costly on scaled manycore chip
WiSync: Leverage on-chip wireless communication for inter-core synchronization

## Slide 3: WiSync Architecture
Each Core has:
L1、L2 Cache
Two Channels: Data & Tone
A Transceiver: PHY, MAC, Tone Controller
Broadcast Memory
Two Bits: WCB & AFB

## Slide 4: Hardware Prerequisite
Wireless Tradeoff
  Area/Power VS Bandwidth
  Bandwidth up, area/power up
  General: 60GHZ 16~20GHZ bandwidth; 90GHZ
  65nm CMOS for 16Gb/s, costs: 0.2mm2 31.2mW
  22nm CMOS for 16Gb/s, costs: 0.1mm2 16mW
Affordable Cost!

## Slide 5: Wireless Transmission
Data Channel
  77 bits per message(64 datum + 11 address + Bulk bit+ Tone bit)
  5 cycles with collision detection(Exponential backoff)
  Bulk bit: send 4 continuous location in bulk(15 cycle)
  Tone bit: For barrier synchronization
Tone Channel
  Manycore synchronization
  Sense-Reversing Barrier
  Multiple concurrent barriers: Time Multiplexing

## Slide 6: Broadcast Memory Management
TLB-like Memory Management
  64bit data + PID tag
  Virtual address translation
  4*4KB page

## Slide 7: Time Multiplexing
Program allocate barrier: AllocBTable(BM Addr + Armed bit)
Program reach barrier: ActiveB copy entry(BM Addr + Arrived bit)
Slot awareness

## Slide 8: Atomic Instruction
Store Synchronization
  Update other nodes first
  Collision and retry
  Update WCB
RMW:
  Test&Set, Fetch&Inc, Fetch&Add, Compare&Swap(CAS)
  Write Completion Bit(WCB)&Atomicity Failure Bit(AFB)
    Read to pipeline, update in pipeline, write back(Collision)
    Updated after read to pipeline: Set AFB

## Slide 9: Evaluation

## Slide 10: CAS Throughput

## Slide 11: Speedup of Application

## Slide 12: Conclusion
Outperform baseline for an order of magnitude
Outperform applications PARSEC&SPLASH-2 1.12X